## Slide 1: uMove
INDIANA UNIVERSITY BLOOMINGTON
Luddy School of Informatics, Computing and Engineering
1
Notes: AJ

## Slide 2: Overview
Team Introduction
Project Overview
System Overview
Objectives and Constraints
Detailed Design Analysis
System Demonstration
Sustainability
Lifelong Learning Goals
Next Steps
2
Notes: AJ

## Slide 3: Team Introductions
SECTION 1
3
Notes: AJ

## Slide 4
Project Coordinator
M.S. Cyber-Physical Systems Fall 2023
Undergraduate Research student at Vehicle Autonomy and Intelligence Lab
ROS, Gazebo, Rviz, Python, C
IT; Cybersecurity Intern at Curia Global
Engineer at Crane, IN
4
AJ Funari
Notes: AJ

## Slide 5
System Manager
B.S. Cyber-Physical Systems Spring 2023
Sensor Unification and Robotics Control
Lead Programmer on Robotics Team
Internship at JFW
Engineer at Crane
5
Ryan Herrington
Notes: Ryan

## Slide 6
Presentation Manager
M.S. Intelligent Systems Engineering
Machine Learning and Embedded Systems
Research Assistant at Socioneural Physiology Lab
Engineer at Crane
6
Isaac Navarrete
Notes: Isaac

## Slide 7
Report Manager
M.S. CPS Spring 2024
Embedded Systems, Machine Learning, Digital Design
Undergraduate Research at Vehicle Autonomy and Intelligence Lab
Internship at Ford Motor Company
7
Ben Bamidele
Notes: Ben

## Slide 8: Project Overview
SECTION 2
8
Notes: Ryan

## Slide 9
Our client, Luddy Outreach, wanted us to develop a system for prospective students to control and engage with using a custom wearable device to help students obtain a better understanding of what ISE students can build using cutting-edge technology at the school of Luddy.
9
Intelligent Systems Engineering! What is it?
Notes: Ryan

## Slide 10
Product/Project Description:
  The overview of our project is to create a wearable device demonstration for Luddy Outreach and Recruiting to help engage with potential ISE students or teach younger students about STEM.
Key Features and/or Operating Modes:
  Our project has two key features, the wearable device, and the demonstration that is used with the device. We have successfully interfaced our wearable device with a custom video game. The device controls via fingertip sensors and an Inertial Measurement Unit (IMU).
Key Differentiating Performance(s):
  A key difference from normal controller to our device is ours in an intuitive interface.
10
uMove
Notes: Isaac

## Slide 11
11
First Chart
Last Chart
Gantt Chart
Notes: AJ

## Slide 12: System Overview
SECTION 3
12
Notes: AJ

## Slide 13
13
Block Diagram
Notes: AJ

## Slide 14: Objectives and Constraints
SECTION 3
14
Notes: Ben

## Slide 15: Objectives
15
Notes: Ben

## Slide 16
System Section | Constraints |  | 
Total System | One person portable | Cannot exceed 15 lbs. | Cannot shock User
Wearable | Battery replaceable | Cannot exceed 2 lbs. | Fit inside case
Case | Rest on table | Safely Secure Glove | Safely contain demonstration
Demonstration | Compatible with wearable | 1-page manual | 2-minute usability
16
Constraints
Notes: Ben

## Slide 17: Detailed Design Analysis
SECTION 5
17
Notes: Isaac

## Slide 18
18
Block 1: Force Transducers and Battery
Purpose
  Create circuit for force transducers
  Collect force transducer data
  Determine wearable power consumption
  Determine battery that will best fit our needs
Block 1: Isaac
Notes: Isaac

## Slide 19
19
Block 1: I/O Summary
Block 1: Isaac
Analog Signal | To-From | Type | Directions | Block-Block Interconnect | Unit | Voltage Nominal | Voltage Min | Voltage Max | Description
Force Transducers | Arduino – Sensor | Analog | Input | Wires | V | 0 - 3.3 | 0 | 3.3 | Collects voltage from fingertips
Power Signals | To-From | Type | Direction | Interconnect | Voltage Nominal | Voltage min | Voltage Max | Freq Nominal | Freq min | Freq Max | % V-reg Max | V-Ripple Max | Current Max
Battery Power | Arduino - Battery | DC | Input | No | 9 | 7.2 | 9.6 | DC | N/A | N/A | 0.01 | 1 | 100mA
Notes: Isaac

## Slide 20
20
Block 1: Design Schematic
Block 1: Isaac
Simple representation of force sensors circuit and hat
Notes: Isaac

## Slide 21
21
Block 1: Battery Calculations
Block 1: Isaac
How long should the device last?
Current Drawn = 0.03 A
Goal Hours = 12 hr
9v Alkaline Battery is rated at ~0.5Ah
  This battery gives ~16 hours of use
Notes: Isaac

## Slide 22
22
Block 1: Verification and Testing
Block 1: Isaac
Testing of force transducers
  Collect data through serial monitor provided by Arduino
Testing of battery
  Use to power Arduino for completely wireless communication
Notes: Isaac

## Slide 23
23
Block 1: Testing Picture
Block 1: Isaac
Notes: AJ

## Slide 24
24
Block 2: IMU
Purpose
  Collect IMU data
  Calculate desired angles
  Data passed off to Bluetooth
Block 2: Ben
Arduino Nano BLE 33
Notes: Ben

## Slide 25
25
Block 2: I/O Summary
Block 2: Ben
Digital Signal | To-From | Type | Directions | Block-Block Interconnect | Unit | Voltage Nominal | Voltage Min | Voltage Max | Description
IMU | Bluetooth – Arduino | Digital | Output | Wires | V | N/A | N/A | N/A | Receives same voltage as Arduino
Notes: Ben

## Slide 26
26
Block 2: IMU
Block 2: Ben
Notes: Ben

## Slide 27
27
Block 2: Testing Picture
Block 2: Ben
Notes: Insert picture of data collection
Ben/Isaac

## Slide 28
28
Block 3: Bluetooth
Block 3: AJ
Purpose
  Allows for a seamless wireless connection
  Transmits wearable device data for control algorithm
  Communicates between the wearable device and the demonstration
Notes: AJ

## Slide 29
29
Block 3: I/O Summary
Block 3: AJ
Digital Signal | To-From Block #'s | Type | Directions | Block-Block Interconnect | Unit | Voltage Nominal | Voltage Min | Voltage Max | Description
IMU | Block 2 – Block 3 | Digital | Input | Wires | V | N/A | N/A | N/A | Receives same voltage as Arduino
Force Transducers | Block 2 – Block 3 | Digital | Input | Wires | V | 0 - 3.3 | 0 | 3.3 | Collects voltage from fingertips
Bluetooth | Block 3 – Block 4 | Digital | Input/Output | Wireless | V | N/A | N/A | N/A | Transmits IMU/sensor data between devices
Notes: AJ

## Slide 30
30
Block 3: Communication Diagram
Block 3: AJ
Notes: AJ

## Slide 31
31
Block 3: Testing and Verification
Block 3: AJ
Light Blue Application
Raspberry Pi
Notes: AJ

## Slide 32
32
Block 4: Demonstration
Block 4: Ryan
Purpose
  Receive data from Bluetooth Handler
  Parse data and convert to keyboard inputs
  Run video game and display for participant
  Hold the screen at an optimal display angle
Notes: Ryan

## Slide 33
33
Block 4: I/O Summary
Block 4: Ryan
Power Signals | To-From | Type | Direction | Interconnect | Voltage Nominal | Voltage min | Voltage Max | Freq Nominal | Freq min | Freq Max | % V-reg Max | V-Ripple Max | Current Max
Wall Input | Converter-Wall Outlet | AC | Input | No | 120 | 102 | 132 | 60 | 57 | 63 | 0.01 | 1 | 1
Converter Input | Raspberry Pi-Converter | DC | Input | No | 5 | 4.75 | 5.25 | DC |  | N/A | 0.01 | 1 | 3
Digital Signals​ | To-From​ | Type​ | Direction​ | Interconnect​ | Coupling​ | Voltage Max​
Bluetooth Data​ | Demonstration - Bluetooth | Digital​ | Input​ | Wireless​ | Wireless​ | N/A​
Notes: Ryan

## Slide 34
34
Block 4: Hardware
Block 4: Ryan
Raspberry Pi 4 Model B
Bluetooth
Raspberry Pi 7” Touch screen
Notes: Ryan

## Slide 35
35
Block 4: Middleware
Block 4: Ryan
Input: Bluetooth Data
Output: keyboard inputs for video game
Notes: Ryan

## Slide 36
36
Block 4: Video Game
Game Engine: Godot
Input: Keyboard
Block 4: Ryan
Output: Game to display
Notes: Ryan

## Slide 37
37
Block 4: Ryan
3 Phases
  Phase 1: Testing game on local computer
  Phase 2: Testing game on Raspberry Pi
  Phase 3: Testing game on Pi with Wearable
Block 4: Testing and Verification
Notes: Ryan

## Slide 38
38
Block 4: Ryan
Testing Phase
3
Testing Phase
2
Testing Phase
1
Block 4: Testing Pictures
Notes: Ryan

## Slide 39
39
AJ
Purpose
  Protect our hardware
  Prevent harm to users
  Provide storage for extra supplies
Prototype Enclosures
Notes: AJ

## Slide 40
40
AJ
Prototype Design – Wearable
Notes: AJ

## Slide 41
41
AJ
Prototype Design – Wearable
Notes: AJ

## Slide 42
42
AJ
Prototype Design – Box
Notes: AJ

## Slide 43
43
AJ
Prototype Design – Box
Notes: AJ

## Slide 44: System Demonstration
SECTION 6
44
Notes: Ryan

## Slide 45
Event Debut
  FIRST Robotics Event March 31st
  Received great feedback
45
FIRST Robotics Demo
Notes: Ryan/AJ

## Slide 46
Power on the device
  Run either Easy_start or Normal_start
    These relate to the level difficulty
  Turn on the wearable by flipping the switch
46
Live Demo
Notes: All show off

## Slide 47: Sustainability
SECTION 7
47
Notes: Isaac

## Slide 48
Alkaline battery will need to be replaced after 16 hours of use
  Batteries can be recycled by Luddy battery disposal bucket, per EPA standards
All our parts are from reputable vendors like DigiKey, Adafruit and Arduino
Easy to replace the force transducers
Arduino microcontroller can be easily overwritten if needed
  Well documented
48
Sustainability
Notes: Isaac

## Slide 49: Lifelong Learning Objectives
SECTION 8
49
Notes: Ben

## Slide 50
We learned a lot about project planning, constraints, project management, game design, and research processes.
Able to collect senor reading from a microcontroller's datasheet to find relevant peripherals
Became familiar with debugging, circuit design, and fabrication
Obtained experience with integrating a Bluetooth network between hardware interfaces.
50
Lifelong Learning Objectives
Notes: Ben

## Slide 51
Lithium-ion battery
Latency
  Arduino
  Bluetooth
  Raspberry Pi
Interface with new demonstration
  Drone
  Differential drive robot
Printed Circuit Board
51
Next Steps
Notes: AJ

## Slide 52
Questions?
52
Notes: All